## Slide 1: VHDL 0 Introduction to VHDL
K H Wong
khwong@cse
3943-8397,
Room 907 SHB-Engineering building
http://www.cse.cuhk.edu.hk/~khwong/www2/ceng3430/ceng3430.html

## Slide 2: CENG3430 Rapid Prototyping of Digital Systems
You will learn:
  The hardware description language VHDL
  Techniques to build a Logic system e.g. building blocks of a Central Processing Unit (CPU)
  High speed logic circuits analysis: time delay estimation, testing, power supply stability, etc.
1 entity and2 is port (a,b : in std_logic;
2 c : out std_logic);
3 end and2
4 architecture and2_arch of and2
5 begin
6 c <=a and b;
7 end and2_arch
Write VHDL code, then
it will generate the hardware chip automatically
Example: A VHDL AND-gate Program
Notes: In this course you will learn a language that can be used to develop hardware.
There are two most popular languages used in the industry, VHDL and Verilog. They are similar so if you know VHDL you can pick up Verilog easily.
VHDl is a powerful language, it can be used to develop CPU or embedded system devices.
Furthermore it can be used to model hardware, that is, finding out the time delay of certain signals.

## Slide 3: A quick run through
Overview

## Slide 4: Overview
What is VHDL used for?
To design
    Hardware systems (an industrial standard)
    Microprocessors: Arm7 etc.
    Design new Digital systems: e.g. mobile phone, camera chips
Notes: VHDL has been used in the industry for companies to design hardware chips.
For example if a company wants to make a new LED TV, a new TV panel hardware is required, designing a new logic circuit is not easy, and it cannot be done by drawing schematics because too many gates are required. The system development work becomes easier if it is designed using a language to describe the hardware.

## Slide 5: Motivations
Learn to design digital systems.
Provide knowledge for you to :
  Design products:
    Robots controllers, media players, portable games, mobile phones.
  Advanced examples
    Image processing
    Computer vision
    Super computer
  Start a business.
Notes: There are design examples on the web including digital MP3 player, robot control systems, digital camera prototypes etc. More advanced examples are , image processing hardware, super-computer design etc.

## Slide 6: Examples of digital system design
Mass products
  Media players
  Mobile phones
Novel products
  Wearable computer
  Robots
Research
  Real time edge detection for computer vision
www.cnn.com/.../06/10/mars.rover/index.html

## Slide 7: To learn
Design digital processing components using programmable logic
  Two existing Methods
    (a) Schematic, (too complicated
      But is suitable to describe the top level design like a data flow block diagram
    (b) Language (e.g. VHDL--Very-High-Speed-Integrated-Circuits Hardware Description Language): Each module in the schematic can be written in VHDL.
1 entity and2 is port (a,b : in std_logic;
2 c : out std_logic);
3 end and2
4 architecture and2_arch of and2
5 begin
6 c <=a and b;
7 end and2_arch

## Slide 8: DIGITAL DESIGN
Work Flow

## Slide 9: Digital Design Work Flow
Idea generation
Drafting on paper
Design the chip (use VHDL)
Test
Manufacturing production line design
Quality control
1 entity and2 is port (a,b : in std_logic;
2 c : out std_logic);
3 end and2
4 architecture and2_arch of and2
5 begin
6 c <=a and b;
7 end and2_arch

## Slide 10: We use In our lab
Hardware: FPGA (Field Programmable Gate Array)
  The hardware can be reprogrammable , so you can change your design rapidly and easily with no additional hardware manufacturing cost.
Software: VHDL (Very-High-Speed-Integrated-Circuits Hardware Description Language)

## Slide 11: Re-programmable Hardware: FPGA Field Programmable Gate Array
So what is inside an FPGA
IOB=Input/Output block
CLB=Configurable Logic block (static ram based)
Change the CLBs to get the desired functions
From http://www.alldatasheet.co.kr/datasheet-pdf/pdf_kor/49173/XILINX/XCS10-3PC84C.html

## Slide 12: Inside a CLB (Configurable Logic block )
The CLB is a fixed design but you can change the logic function for generating output from input G1-G4 by reprogramming the bits in the logic function lookup table.
This will change the overall logic function of the CLB
Re-programming the logic table
http://www.design-reuse.com/news_img/20100913_1.gif
http://pldworld.biz/html/technote/pldesignline/bobz-02.gif
CLB
FPGA CLB
(Configurable Logic block )

## Slide 13: Example: Virtex-II Architecture
Virtex™-II architecture’s core voltage operates at 1.5V
I/O Blocks (IOBs)
Configurable
Logic Blocks (CLBs)
Clock Management (DCMs, BUFGMUXes)
Block SelectRAM™
resource
Dedicated multipliers
Programmable interconnect
www.eece.unm.edu/course/ece338/Lectures/basic-fpga-arch-xilinx.ppt
Notes: This is a graphical view of the resources of an FPGA (specifically, resources available for the Virtex™-II device).
The block SelectRAM™ resources are located between the CLBs, next to the dedicated multiplier. Programmable interconnect connects the CLBs. The CLBs contain combinatorial logic functions and sequential elements. Most, if not all, of the logic in a design is contained in CLBs.
The I/Os interface the FPGA with other devices on the system board. The core voltage of Virtex-II is 1.5V. The I/Os can operate at different voltages, depending on the I/O type you choose.

## Slide 14: Software: to program an FPGA
1 entity and2 is port (a,b : in std_logic;
2 c : out std_logic);
3 end and2
4 architecture and2_arch of and2
5 begin
6 c <=a and b;
7 end and2_arch
Use a schematic: (Top level design to merge modules)
Use a language VHDL (for each
module)
or/and

## Slide 15
FPGA
development
Schematic /
VHDL
simulation
1 entity and2 is port (a,b : in std_logic;
2 c : out std_logic);
3 end and2
4 architecture and2_arch of and2
5 begin
6 c <=a and b;
7 end and2_arch
Development cycle
VHDL language
Schematic (diagram)

## Slide 16: Test bench and timing simulation use simulation to see if your design is correct or not.
See the tutorial at http://www.cse.cuhk.edu.hk/~khwong/www2/ceng3430/CENG3430_1617_Tutorial_1_7a_test_bench.pptx
You create some input patterns and see if the outputs are behaving correctly or not
Inputs
outputs

## Slide 17: Summary of VHDL
For hardware Design
Parallel language (not sequential)
Different! (not the same as C++ or Java)
VHDL is the industrial standard for CE.

## Slide 18: An example: “And” gate in VHDL
1 entity and2 is port (a,b : in std_logic;
2 c : out std_logic);
3 end and2
4 architecture and2_arch of and2
5 begin
6 c <=a and b;
7 end and2_arch
Entity declaration: define IOs
Architecuture
body: functional definition
Enitity
a
b
c
The chip
C<=a and b

## Slide 19: Computer Engineering Market
and VHDL

## Slide 20: TSMC (Taiwan Semicon. Manufacturing Comp.) 台灣積體電路製造股份有限公司 http://www.tsmc.com
From Wiki:
  Has the largest asset in Taiwan stock market,
  One of the World's largest dedicated independent semiconductor foundry.
  Products: Apple iphone6 plus A8-cpu
Relation to VHDL
  Design ideaWrite VHDL  TSMC chips

## Slide 21: Huawei Technologies Co. Ltd http://www.huawei.com/en/
From wiki:
  Telecom equipment manufacture
  China large private company--http://money.163.com 500 (2011-08-25)
  Products: the second-largest supplier of mobile telecommunications infrastructure equipment in the world (after Ericsson).

## Slide 22: References
See course web page
Digital Systems Design Using VHDL, Charles H. Roth (first or second edition)
Rapid Prototyping of Digital Systems, by Hamblen, James etal. Springer 2008. (read_online)
Digital Design: Principles and Practices, 4/E John F. Wakerly, Prentice Hall.
High-Speed Digital Design: A Handbook of Black Magic by Howard W. Johnson and Martin Graham Prentice Hall.
BOOKBOON (Free text books)
http://www.alldatasheet.com/

## Slide 23: Appendix

## Slide 24: Major companies , a comparison in 2011 (from wiki)
Company | Boeing | Nestle | Honda | Toyota | Ford | HSBC | Lenovo | BP | Sony
Revenue US Billion | 68.5 | 125 | 120 | 235 | 128 | 98.9 | 21.59 | 308.9 | 86.64
Asset | 64.3 | 126 | 125 | 370 | 166 | 2454 | 10.71 | 272.2 | 155.94
Profit US Billion | 3.3 | 39 | 1.39 | 5.07 | 6.56 | 13.15 | 0.273 | 3.3 | 2.96

## Slide 25: (from wiki) Wiki: 2009年資本額約新台幣2,589.6億元,市值約1兆6,000億元，為台灣股市中市值最大的公司。http://money.163.com 中国民营企业500强榜单发布,华为第一 (2011-08-25)
Company | Apple | IBM | Microsoft | Intel | HP | TSMC 台灣積 體電路 (largest asset in Taiwan stock market) | Huawei 华为(Telecom equipm’t, China large private company)
Revenue US Billion | 65.23 | 99 | 69.94 | 43.6 | 99.87 | 13.98 | 21.8
Asset | 75.1 | 113.5 | 108.7 | 63.2 | 124.5 | 20.43 | Not known
Profit US Billion | 14.01 | 14 | 23.15 | 11.46 | 14.83 | 5.55 | 2.67

## Slide 26: Tri-state Logic
A revision:’
The concept of tri-state logic is essential in computer design, so we want to revise these techniques before we move on.

## Slide 27: Appendix 1:Tri-state logic **At the float state, the wire is cut
Input
Output
enable (OE)
Output

## Slide 28: Tri-state equivalent circuit (using output connect/cut view)
Input
Output
enable (OE)
Output
Input
Output
enable (OE)
Output
OE=1, switch close
OE=0, switch open
Same as

## Slide 29: Alternatively: we can treat the Tri-state equivalent circuit using the Rout impedance view
Input
Output
enable (OE)
Output
Input
Output
enable (OE)
Output
When OE=1, Rout= small, (e.g. 50 Ω )
When OE=0, Rout=infinity (e.g. 10 MΩ)
Same as
Rout
OE (output enable)
controls the value
of Rout
Tri-state equivalent circuit :
Rout impedance view
to explain the concept of tri-stat
A tri-state circuit diagram

## Slide 30: Student ID: ___________,Date:_____________ Name: _______________ Exercise0.1:Tri-state logic with pull up resistor
Input1
Output-Enable (OE)
Output
5V
10K
**At float the wire
is cut

## Slide 31: Exercise0.2: Use Rout ( Impedance view) to explain the result of exercise 0.1
Resistance view

## Slide 32: Exercise 0.3 Application 1 of Tri-state logic: Input/Output pin
OE1 controls the traffic.
Fill in the cells with ‘?’.
Directional
control(OE1)
A
B

## Slide 33: Exercise 0.4 Application 2 of Tri-state logic: Transceivers for I/O data pins
When T =1, A->B; T controls the traffic,
when /OE=1, IO pins A,B are disabled
Fill in the cells with ‘?’.
A
B
/OE
T

## Slide 34: All data-lines are transceiver buffers
A good controller will enable the CPU to
read/write RAM, and read ROM
CPU data lines
transceivers
ROM
data
lines
RAM
data
lines
transceivers
transceivers
/OE1, T1
/OE2, T2
/OE3,
T3

## Slide 35: Exercise 0.5 : List OE1,2,3 and T1,2,3 for the followings cases
a) CPU writes to RAM:
  /OE1=___ , /OE2___, /OE3=___, T1___, T2=____, T3_____
b) CPU reads from ROM
  /OE1=___ , /OE2___, /OE3=___, T1___, T2=____, T3_____
c) CPU reads from RAM
  /OE1=___ , /OE2___, /OE3=___, T1___, T2=____, T3_____
CPU data lines
transceivers
ROM
data
lines
RAM
data
lines
transceivers
transceivers
/OE1, T1
/OE2, T2
/OE3,
T3
A
B
A
B
B
A

## Slide 36: Exercise 0.6 Application 3 of Tri-state logic: Selection of control signal (resolved logic)
Output depends on Input_A if OE is _?___
Output depends on Input_B if OE is _?___
Discuss the operation of this circuit.
Input_B
Input_A
Output
OE

## Slide 37: Exercise 0.7
Fill in ‘?’. Is it a “nor-gate” or an “or-gate”?
Discuss the operation of this circuit.
Answer :
Output
OE2
5V
10K
OE1
0V
0V